## Slide 1
National Institute of Technology Karnataka Surathkal
Automatic Door Lock Security System
R Jivith Abhishek
Galegave Ajinkya Arjun
Rohanraj Shinde
Submitted By
Group 22
Submitted To
Dr. B. Dastagiri Reddy

## Slide 2
Overview
  Introduction
  Components
  Working of components
  Model Explanation
  Scope
  References

## Slide 3
Introduction
  In the current era of new technology, comes security breaches to personal data.
  So to protect it we have to find an alternative to older locks.
  So here we come up with password protected door lock security system with alarm.

## Slide 4
Components
Component
Quantity
Arduino UNO Dev Board 1
Solenoid Lock (12V) 1
Relay (5V) 1
Numeric Keypad 1
12 V lithium Ion Battery 1
Breadboard 1
LED (20mA) 1
Resistor 2
Buzzer 1
Jumper wires -

## Slide 5
What is a solenoid ?
A solenoid is a long helical coil of wire through which a current is run in order to create a magnetic field. The magnetic field of the solenoid is the superposition of the fields due to the current through each coil. It is nearly uniform inside the solenoid and close to zero outside and is similar to the field of a bar magnet having a north pole at one end and a south pole at the other depending upon the direction of current flow.

## Slide 6
When an iron core is placed in the solenoid, it becomes magnetized and is drawn into the solenoid, compressing the spring and allowing the door to unlock. When the power supply is cut, the iron core demagnetizes, causing the spring to expand and pushing the iron core back out to lock the door
Working of a solenoid Lock

## Slide 7
Model Explanation
  To open the door lock, we have to enter the correct password on the keypad.
  Once we enter the correct password, the Arduino sends the signal to Relay Module
  The Relay Module acts like a switch and allows the current to pass from the 12V battery to solenoid.
  The door opens with one Beep and yellow LED Blink.
  The door automatically close after a time interval of 3 seconds.

## Slide 8
Model Explanation
  Now we have enhanced security by introducing alarm whenever someone enters wrong password.
  So when the password entered is incorrect, the door remains closed and the Buzzer sounds and LED blinks 4 times continously.

## Slide 9
CIRCUIT DIAGRAM

## Slide 10
Scope
The main scope of application of the Automatic door lock security system is offices, warehouses, and home.
There are certain situations that are very annoying like a person locks himself out of the house or the key to the door is lost. These kinds of situations always trouble people with manual locks.
Although in some places people use smart cards(RFID) but someone can lose the card.
That is when Password based automatic door lock system comes into play.

## Slide 11
References
  https://www.youtube.com/watch?v=BLrHTHUjPuw&t=2s
  https://playground.arduino.cc/Code/Keypad/https://playground.arduino.cc/Code/Keypad/